Town of Swanton

2015 GARAGE FENCING REQUEST FOR BIDS

The Town of Swanton is requesting bids for the installation of a chain link fence and a gate for its Garage Complex at 221 First Street.

FENCING REQUIREMENTS:

- Provide labor & materials for a 6 foot high chain link fence & gate at the Town of Swanton Garage Complex at 221 First Street.

- Fence posts to be galvanized steel.

- Gate to be galvanized or aluminum.

- Gate to have remotely operated automatic opener with 6 remotes provided.

- Provide a Knox Box at the gate with an electric button inside the Knox box to open the gate.

- Include the cost of all electrical work in the bid price.

- Fence to be installed as illustrated on the attached drawing.  Exact locations of the corners to be determined on site. The Town will do all tree & brush clearing that is needed.

- Please provide a separate bid for each of the following options:

  - OPTION ONE – 6’ high fence with 5’ high aluminum gate (25’ opening)

  - OPTION TWO - 6’ high fence with 5’ high aluminum gate (20’ opening)

  - OPTION THREE - 6’ high fence with galvanized gate (25’ opening)

  - OPTION FOUR - 6’ high fence with galvanize gate (20’ opening)

  - OPTION FIVE – Delete fence on north side except for the first 20’ from each corner.

- WARRANTY:  Provide a warranty guaranteeing that fence & front entrance gate will be free from defects in materials and workmanship for three years.

- NOTE: Vermont municipalities are sales tax exempt.

BIDDERS:

Contractors are required to have the appropriate equipment, experience & insurance for the work to be done.  Please note that the accompanying aerial photo sketch does not have all existing buildings shown on it. The award of the contract to a firm to perform the fence & gate  construction will be made on technical merit, estimated time frame, and responsiveness to the scope of requirements listed above. Comparative cost estimates will be considered but will not be the sole basis for selection of the bidder. The Town of Swanton reserves the right to reject any or all proposals received, to negotiate with any qualified bidder, and to cancel in part or its entirety this Request for Proposals if it determines that it is not in the best interest of the Town of Swanton. This solicitation in no way obligates the Town of Swanton to award a contract to any firm responding to this Request for Bids.

Questions and an appointment for a site visit should be directed to Highway Foreman, Harold Garrett, by calling 802-752-7138 or emailing him at highwaydept@swantonvermont.org or to Town Administrator, David Jescavage, by calling 802-868-7418 or emailing him at townadmin@swantonvermont.org .

All proposals shall be due on Tuesday, May 5, 2015 at 4 p.m. by U.S. Mail, hand delivery, or parcel delivery (no emails or faxes will be accepted)(proposals must arrive at the Town Office Building by the deadline) to the address below:

Swanton Garage Fence Project

David Jescavage, Town Administrator

P.O. Box 711, 1 Academy Street

Swanton, VT 05488

GARAGE COMPLEX LOCATION MAP